Emulating a Sega Master System
in Javascript

---
Why?

---
Back story
- SMS/Megadrive confusion
- Miracle ARM version

---
What's inside
- Z80 CPU
- 8KB RAM
- Custom Video Chip
  - based on Texas Instrument part
- SN76489 Sound Chip

---
Z80
- CISC chip
  - ~900 instructions
  - no multiply, no divide
- ~3.5MHz
  - but long instruction times...
    - 7 cycles for “LD A, constant”
    - 1.75us
- 18 8-bit registers
  - General purpose: A, B, C, D, E, H, L
  - Alternate: A', B', C', D', E', H', L'
  - Flags: F, F'
  - IRQ, Memory Refresh: I, R
  - Can be paired and treated at 16-bit
    - AF, BC, DE, HL
- 4 16-bit registers
  - Index registers: IX, IY
  - Stack: SP
  - PC

---
Memory Map
- Picture here, ROM paging etc
- readbyte implementation?

---
Z80 – Decoding
- Optional prefix (0xcb, 0xdd, 0xed, 0xfd)
- Opcode byte
- Operand bytes (0-2)
- Examples
  - XOR A, A → af
  - LD A, 0xff → 3e ff
  - LD B, (IX + 0x0f) → dd 46 0f
  - LD DE, (0xd019) → ed 5b 19 d0
  - simple loop example?

---
Z80 – Executing
- Arithmetic – easy:
  - ADD A, 0x80
  - regs.a += 0x80 ?
- Flags
  - overflow, parity
  - carry, half-carry
  - add/subtract
  - zero, sign

---
Z80 – Executing
- Complex!
- Based on open source code from JSSpeccy
- which was based on a Speccy (written in C)

---
Back to example:
  - var bytetemp = 0x80; // or whatever
  - var addtemp = z80.a + bytetemp;
  - var lookup = ((z80.a & 0x88) >> 3 ) | ((bytetemp & 0x88) >> 2 ) | ((addtemp & 0x88) >> 1);
  - z80.a = addtemp & 0xff;
  - z80.f = (addtemp & 0x100 ? FLAG_C : 0) // Carry bit
  - | halfcarry_add_table[lookup & 0x07] // Half carry
  - | overflow_add_table[lookup >> 4] // overflow
  - | sz53_table[z80.a]; // sign, zero, “undefined” bits
- Z80 – Execution
  - Take instruction tables
  - PERL script to generate jscpp
  - ...then preprocessed to javascript
  - Avoids lots of repetitive code
  - 938 instructions
  - 1241 lines of perl
  - 5400 lines of javascript generated
- VDP
  - 16KB of RAM
  - 8x8 “tiles”
    - 4 bits per pixel
      - 16 colours from one of two palettes
    - Planar
  - 32 entry palettes of 6-bit colour
  - 32 x 24 background map of tiles
    - Two bytes per tile
      - 9 bits tile index (512)
      - 2 bits vertical, horizontal flip
      - 1 bit palette select
      - 1 bit sprite overwrite
      - 3 user bits
  - Sprites
    - 64 sprites
    - 8x8 or 8x16
    - 256 byte table sets X, Y and tile index
      - Can only be one of first 256 tiles
      - All use palette 2
      - 64 bytes “spare” … some games pack more tiles in here
- Sound!
- Putting it all together
- Bug fixing
  - debugging
- Optimization
- Future direction
  - YM2413
  - GameGear
  - Save games
- BBC Emulator...